## Slide 1: MODULE-II INPUT/OUTPUT ORGANIZATION
By,
Mrs. Ashwini Janagal
Department of AIML
JNN College of Engineering

## Slide 2
ACCESSING I/O DEVICES

## Slide 3: ACCESSING I/O DEVICES
Bus
I/O de
vice 1
I/O de
vice
n
Processor
Memory
Single Bus Architecture
BUS
DATA LINES
ADDRESS LINES
CONTROL LINES

## Slide 4: ACCESSING I/O DEVICES
BUS
DATA LINES
ADDRESS LINES
CONTROL LINES
If Processor Wants to Send/Receive any Data from some I/O device...........................
PROCESSOR
DATA LINES
ADDRESS LINES
CONTROL LINES
PROCESSOR will keep ADDRESS of the device on ADDRESS LINE
DEVICE will identify its ADDRESS and respond on CONTROL LINE
FINALLY data transaction will happen on DATA LINE

## Slide 5: ACCESSING I/O DEVICES
BUS
DATA LINES
ADDRESS LINES
CONTROL LINES
How do you address I/O devices?
I/O ADDRESSING
I/O and MEMORY with SAME ADDRESS SPACE
SEPARATE
I/O ADDRESS SPACE
Called as “MEMORY MAPPED I/O”.
SAME INSTRUCTIONS to access MEMORY and I/O.
Simple.
If DATAIN is KEYBOARD REGISTER, LOCA is MEMORY LOCATION.
MOVE DATAIN, R0;
MOVE LOACA, R1

## Slide 6: ACCESSING I/O DEVICES
BUS
DATA LINES
ADDRESS LINES
CONTROL LINES
How do you address I/O devices?
I/O ADDRESSING
I/O and MEMORY with SAME ADDRESS SPACE
SEPARATE
I/O ADDRESS SPACE
  SPECIAL INSTRUCTIONS to transfer data to and from I/O devices.
  Ex: Some INTEL Versions have separate 16 bit ADDRESS for I/O DEVICES.
  I/O address lines need not be physically separate from memory address lines.

## Slide 7: ACCESSING I/O DEVICES
I/O
int
erface
decoder
Address
Data and
status registers
Control
circuits
Input device
Bus
Address lines
Data lines
Control lines
Decoding the address sent by Processor to enable device to identify itself.
Data register holds the Data Being Transferred -- to or from the processor.
Status register holds information necessary for the operation of the I/O device.

## Slide 8: ACCESSING I/O DEVICES
I/O
int
erface
decoder
Address
Data and
status registers
Control
circuits
Input device
Bus
Address lines
Data lines
Control lines
Always remember -- I/O devices are very slow compared to memory and processor.
Synchronization is required.
Ex: SIN flag in Keyboard STATUS REGISTER.
  SIN=1, Data (Character) is READY at KEYBOARD REGISTER
  SIN=0, after DATA is READ FROM PROCESSOR.

## Slide 9: ACCESSING I/O DEVICES

## Slide 10: ACCESSING I/O DEVICES
STATUS IN and OUT for KEYBOARD AND DISPLAY.
DIRQ-> DISPLAY Interrupt Request
KIRQ-> KEYBOARD Interrupt Request
DEN --> DISPLAY ENABLE
KEN --> KEYBOARD ENABLE

## Slide 11
INTERRUPTS

## Slide 12: INTERRUPTS-INTERRUPT HARDWARE
Three Ways to Access I/O Devices
Program Controlled I/O
Interrupts
Direct Memory Access (DMA)

## Slide 13: INTERRUPTS-INTERRUPT HARDWARE
Three Ways to Access I/O Devices
Program Controlled I/O
Interrupts
Direct Memory Access (DMA)

## Slide 14: INTERRUPTS-INTERRUPT HARDWARE
What is an Interrupt?
Answer: A COMMUNICATION SIGNAL to let know that Input/Output device is ready.
INTERRUPT REQUEST LINE
A BUS CONTROL LINE to send INTERRUPT.
INTERRUPT SERVICE ROUTINE
A subroutine called in response to INTERRUPT.

## Slide 15: INTERRUPTS-INTERRUPT HARDWARE
EXAMPLE
Consider a program consisting of two functions. ‘COMPUTE” and “PRINT”.
“COMPUTE” : Will generate an output of 100 lines.
“PRINT”: Will print the lines. One line at a time.
  “PRINT” will send one line and wait for Printer to finish the task. Then Next Line will be sent.

## Slide 16: INTERRUPTS-INTERRUPT HARDWARE
So....What Happens at This Location?

## Slide 17: INTERRUPTS-INTERRUPT HARDWARE
Execution Control has to jump to Interrupt Service Routine
Before Branching Store the current values of
Program Counter (PC)
Processor Registers.
Control Flags

## Slide 18: INTERRUPTS-INTERRUPT HARDWARE
Saving and Restoring may be done Automatically
Its Time Consuming

## Slide 19: INTERRUPTS-INTERRUPT HARDWARE
Interrupt Latency
Time taken from Interrupt Reception to Start of Interrupt Service routine.
How do you reduce Latency?
1. Processor Automatically store only minimum information.
2. Rest if necessary user in program has to add extra instructions.

## Slide 20: INTERRUPTS-INTERRUPT HARDWARE
INTERRUPT-HARDWARE
There are Multiple I/O Devices Connected. Can they send Interrupts together? How this will be handled?
No Interrupt :
I/P=Vdd
INTR=0
Interrupt From Any Device:
I/P=0
INTR=1

## Slide 21: INTERRUPTS-INTERRUPT HARDWARE
INTERRUPT-HARDWARE
There are Multiple I/O Devices Connected. Can they send Interrupts together? How this will be handled?
WHAT ARE THE ISSUES NOT SOLVED HERE??????

## Slide 22: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. What if Processor Doesn’t want to be Interrupted?
2. Interrupts can come at any time and change the course of execution. So they need some controlling.
3. Interrupt from keyboard is acceptable only when there is an editor program running.

## Slide 23: INTERRUPTS-INTERRUPT HARDWARE
After receiving Interrupt Signal how does processor let that device know that “Wait, I have received your signal” ?
Interrupt Acknowledgement Signal - Sent by Processor.
Start of Data Transfer will let that device know. Why I have to send an acknowledgement?

## Slide 24: INTERRUPTS-INTERRUPT HARDWARE
What if Processor Doesn’t want to be Interrupted?
When Interrupt Service Routine is Executing ---- Other interrupt should not come....
First Line of Service Routine- Disable Request Line
Last Line of Service Routine - Enable Request Line

## Slide 25: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 1: Interrupt from Single Device
Step 1: Keep Interrupt signal high until Processor Accepts it. i.e., until execution of Service Routine
Step 2: Signal is high.... should not be considered as another interrupt as it lead to infinite loop.
Step 2.1: Ignore Until Execution of First Line of Service Routine
Step 2.2: Disable Interrupt Request Line
Step 2.2: Execute remaining service routine
Step 2.2: At the end Enable request line
METHOD-1

## Slide 26: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 1: Interrupt from Single Device
Step 1: Keep Interrupt signal high until Processor Accepts it. i.e., until execution of Service Routine
Step 2: Signal is high.... should not be considered as another interrupt as it lead to infinite loop.
Step 2.1:Processor Automatically DISABLE the request line
METHOD-2

## Slide 27: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 1: Interrupt from Single Device
HOW TO ENBALE/DISABLE DEVICES?
1. PROCESSOR STATUS REGISTER(PS) : To indicate status of register
2.
a. INTERRUPT-ENABLE-BIT in PS register=1, means Interrupt enabled
b. INTERRUPT-ENABLE-BIT in PS register=0, means Interrupt Disabled.

## Slide 28: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 1: Interrupt from Single Device
Edge Triggered Interrupt Request Line: Leading edge of signal Activates Interrupts.
Only once INTERRUPTS are registered.

## Slide 29: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 1: Interrupt from Single Device
SUMMARY
1. Device raises an Interrupt.
2. Processor Interrupts current running program.
3. INTERRUPT DISABLE by changing PS bits.
4. Interrupt Acknowledgement.
5. Interrupt Service Routine is Run
6. INTERRUPT ENABLE

## Slide 30: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Imagine the devices connected to processor with single shared bus

## Slide 31: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Imagine the devices connected to processor with single shared bus
INTERRUPT HAS COME FROM WHICH DEVICE???????????

## Slide 32: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Imagine the devices connected to processor with single shared bus
WHICH SERVICE ROUTINE TO EXECUTE??????

## Slide 33: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Imagine the devices connected to processor with single shared bus
ALREADY ONE DEVICE INTERRUPT SERVICE ROUTINE IS EXECUTING......SHOULD OTHER DEVICE BE ALLOWD TO SEND INTERRUPT NOW????????

## Slide 34: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Imagine the devices connected to processor with single shared bus
WHAT IF TWO THREE DEVICES SEND INTERRUPT AT SAME TIME?

## Slide 35: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
SIMPLE WAY TO FIND WHICH DEVICE IS HAS SENT INTERRUPT - POLLING
1. CHECK the STATUS register of each device.
2. If IRQ bit is 1, then that device has sent Interrupt.
3. POLL All the devices connected, and in order if IRQ bit=1, then run that devices SERVICE ROUTINE.

## Slide 36: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
VECTORED INTERRUPT
1. Even though POLLING is simple, it wastes lot of time in POLLING.
2. VECTORED INTERRUPT- INTERRUPTING DEVICE will IDENTIFY ITSELF by sending some CODE.
3. PROCESSOR will directly start EXECUTING respective SERVICE ROUTINE

## Slide 37: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
VECTORED INTERRUPT
1. Even though POLLING is simple, it wastes lot of time in POLLING.
2. VECTORED INTERRUPT- INTERRUPTING DEVICE will IDENTIFY ITSELF by sending some CODE.
3. PROCESSOR will directly start EXECUTING respective SERVICE ROUTINE
WHAT IS THE CODE SENT???????

## Slide 38: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
VECTORED INTERRUPT
1. Even though POLLING is simple, it wastes lot of time in POLLING.
2. VECTORED INTERRUPT- INTERRUPTING DEVICE will IDENTIFY ITSELF by sending some CODE.
3. PROCESSOR will directly start EXECUTING respective SERVICE ROUTINE
WHAT IS THE CODE SENT???????
MAY BE STARTING ADDRESS OF SERVICE ROUTINE
Its size may vary from 4 to 8 bits.

## Slide 39: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
VECTORED INTERRUPT
1. The location pointed by Interrupting device is where STARTING ADDRESS of SERVICE ROUTINE is stored.
2. INTERRUPT VECTOR: Vector of STARTING ADDRESS OF SERVICE ROUTINES.

## Slide 40: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
VECTORED INTERRUPT
How is VECTOR code sent ???????

## Slide 41: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
VECTORED INTERRUPT
1. DATA BUS is used.
2. DEVICE will RISE INTERRUPT REQUEST
3. DEVICE will WAIT until INTERRUPT ACKNOWLEDGEMENT.
4. DEVICE will SEND the CODE over DATA BUS.
How is VECTOR code sent ???????

## Slide 42: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
INTERRUPT NESTINBG
1. What if there is an INTERRUPT REQUEST which can’t be IGNORED.
PRESSURE OF SOME UNIT IN A FACTORY IS IN DANGER LEVEL
THERE IS SOME ROBBER OPENING THE DOOR OF BANK.... SESOR IS SENDING THE SIGNAL.....

## Slide 43: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
INTERRUPT NESTING
1. What if there is an INTERRUPT REQUEST which can’t be IGNORED.
2. That means, some I/O devices are not so important so they should not interfere.
3. But some I/O devices are very important and as and when they want their INTERRUPT SIGNAL should be handled.

## Slide 44: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
INTERRUPT NESTINBG
1. What if there is an INTERRUPT REQUEST which can’t be IGNORED.
2. That means, some I/O devices are not so important so they should not interfere.
3. But some I/O devices are very important and as and when they want their INTERRUPT SIGNAL should be handled.
How to DESIGN THIS????

## Slide 45: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
INTERRUPT NESTINBG
1. Give a PRIORITY to each device.
PRIORITY OF PROCESSOR IS PRIORITY OF THE PROCESS IT IS EXECUTING

## Slide 46
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
INTERRUPT NESTINBG
1. Give a PRIORITY to each device.
PROCESSOR PRIORITY is a code in PROCESSOR STATUS (PS) REGISTER.
INTERRUPTS-INTERRUPT HARDWARE

## Slide 47: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
INTERRUPT NESTINBG
1. Give a PRIORITY to each device.
We can change PRIORITY using PRIVILEGED INSTRUCTIONS.

## Slide 48: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
INTERRUPT NESTINBG
1. Give a PRIORITY to each device.
We can change PRIORITY using PRIVILEGED INSTRUCTIONS.
Do you know about PRIVILEGED EXCEPTION

## Slide 49: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
When an INTERRUPT SERVICE ROUTINE is executing, if another INTERRUPT comes then,
  i. INTERRUPT REQUEST is from a device with LOWER PRIORIRTY compared to the present one then IGNORE IT.
  ii. INTERRUPT REQUEST is from a device with HIGHER PRIORIRTY compared to the present one then stop this one and EXECUTE the SERVICE ROUTINE of NEW REQUEST.

## Slide 50: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES

## Slide 51: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Handling Simultaneous Requests
INTERRUPT REQUEST
INTERRUPT ACKNOWLEDGEMENT

## Slide 52: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Handling Simultaneous Requests
INTERRUPT REQUEST
INTERRUPT ACKNOWLEDGEMENT

## Slide 53: INTERRUPTS-INTERRUPT HARDWARE
Enabling and Disabling Interrupts
1. Case 2: HANDLING MULTIPLE DEVICES
Handling Simultaneous Requests
INTERRUPT REQUEST
INTERRUPT ACKNOWLEDGEMENT

## Slide 54: INTERRUPTS-INTERRUPT HARDWARE
Controlling Device Requests
  1. Which Device will raise Interrupt?
  Only the devices which are used by current programs. (What happens when you press keyboard keys when no editor program is running????)
  2. How will you tell other devices that they are not allowed to send Interrupts?
  DEN (Display Enable) and KEN (Keyboard Enable) will do it.

## Slide 55: INTERRUPTS-INTERRUPT HARDWARE
Controlling Device Requests
  1. Which Device will raise Interrupt?
  Only the devices which are used by current programs. (What happens when you press keyboard keys when no editor program is running????)
  2. How will you tell other devices that they are not allowed to send Interrupts?
  DEN (Display Enable) and KEN (Keyboard Enable) will do it.
  If DEN=1 then the display can set DIRQ=1 to rise an interrupt.

## Slide 56: INTERRUPTS-INTERRUPT HARDWARE
Controlling Device Requests
  Example: Write the steps to perform the following operations.
  Consider a Processor where SERVICE ROUTINE is stored in location INTVEC.
  IE (Interrupt Enable) in Processor status register is Bit 9.
  PROBLEM:
  Read a line in From KEYBOARD and store the characters (1 Byte each) from memory location LINE.

## Slide 57: INTERRUPTS-INTERRUPT HARDWARE
Controlling Device Requests
  Step 1: Load Starting Address of SERVICE ROUTINE in INTVEC.
  Step 2: Load starting address of LINE in PNTR.
  Step 3: Enable Keyboard Interrupt service (KEN=1).
  Step 4: Enable Interrupts in processor by setting IE=1

## Slide 58: INTERRUPTS-INTERRUPT HARDWARE
Controlling Device Requests
  Step 5: When key is pressed Interrupt Request is issued. Service routine will read the data from register and make KIRQ=0;
  Step 6: Read character will be placed in location pointed by PNTR and Increment PNTR.
  Step 7: On reaching EOL (END OF LINE) Disable Keyboard Interrupt (KEN=0) and inform the program.
  Step 8: Return;

## Slide 59: INTERRUPTS-INTERRUPT HARDWARE
EXCEPTIONS
What is an Exception?
Any Event that causes Interruption to the execution of any program.

## Slide 60: INTERRUPTS-INTERRUPT HARDWARE
EXCEPTIONS
Which are the different kinds of Exception?
1. “Interrupt from I/O device” is also an exception.
2. Recovery from error: Some instruction level error/Operation level error, processor will rise exception.
3. Debugging: A program, which helps the programmer to find errors. With the help of Exception it provides “TRACE” and “BREAKPOINT”

## Slide 61: INTERRUPTS-INTERRUPT HARDWARE
EXCEPTIONS
Which are the different kinds of Exception?
1. “Interrupt from I/O device” is also an exception.
2. Recovery from error: Some instruction level error/Operation level error, processor will rise exception.
3. Debugging: A program, which helps the programmer to find errors. With the help of Exception it provides “TRACE” and “BREAKPOINT”
In TRACE mode Exception happens after the execution of every instruction.
After every execution, it will allow us to check variable values, register contents etc.

## Slide 62: INTERRUPTS-INTERRUPT HARDWARE
EXCEPTIONS
Which are the different kinds of Exception?
1. “Interrupt from I/O device” is also an exception.
2. Recovery from error: Some instruction level error/Operation level error, processor will rise exception.
3. Debugging: A program, which helps the programmer to find errors. With the help of Exception it provides “TRACE” and “BREAKPOINT”
Instead of every Instruction, Breakpoints will be set for specific instructions and exception will happens only when execution reaches that point.

## Slide 63: INTERRUPTS-INTERRUPT HARDWARE
EXCEPTIONS
Which are the different kinds of Exception?
1. “Interrupt from I/O device” is also an exception.
2. Recovery from error: Some instruction level error/Operation level error, processor will rise exception.
3. Debugging: A program, which helps the programmer to find errors. With the help of Exception it provides “TRACE” and “BREAKPOINT”
Suppose you set “BREAKPOINT” for instruction ‘i’, then DEBUGGER will replace ‘i+1’ with SOFTWARE INTERRUPT.
This SOFTWARE INTERRUPT” will help in checking the intermediate values. When user is done original i+1 instruction will be reloaded.

## Slide 64: INTERRUPTS-INTERRUPT HARDWARE
EXCEPTIONS
Which are the different kinds of Exception?
1. “Interrupt from I/O device” is also an exception.
2. Recovery from error: Some instruction level error/Operation level error, processor will rise exception.
3. Debugging: A program, which helps the programmer to find errors. With the help of Exception it provides “TRACE” and “BREAKPOINT”.
4. Privileged Instructions: “ Instructions” which can be executed only when processor is running in supervisor mode.
If anyone try to execute “PRIVILEGED INSTURCTION” the “PRIVILEGED EXCEPTION” will be raised.

## Slide 65: INTERRUPTS-INTERRUPT HARDWARE
EXCEPTIONS
What happens when Exception is raised?
Same as Interrupts, Current process is suspended and Exception Handling subroutine will be called.

## Slide 66: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
  OS is responsible for coordinating all the activities of the computer.
  OS uses INTERRUPTS to perform following operations.
    Assign Priorities
    Switch between different user programs.
    Security and Protection

## Slide 67: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
  Application Programs (Software that we create) depends on OS for many things, for example I/O device communication.
  When APPLICATION has to perform I/O, it requests OS.
  OS will perform I/O by using Interrupts.

## Slide 68: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
  Application Programs (Software that we create) depends on OS for many things, for example I/O device communication.
  When APPLICATION has to perform I/O, it request OS.
  OS will perform I/O by using Interrupts.
OS provides various services.
How does your program find out about the services?
  Each service has a “SOFTWARE INTERRUPT INSTRUCTION” calling which will execute an “SERVICE ROUTINE” whose addresses are maintained by Processor in vector format.
  OR we may use “ONE INSTRUCTION WITH DIFFRENET OPERANDS”

## Slide 69: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
Switching from “USER MODE” to “SUPERVISOR MODE” for “INTERRUPT” by setting a bit in “PROCESSOR STATUS REGISTER”
  So when Interrupt Request comes, processor switches to supervisor mode to give OS complete access to resources.
  After returning from “SERVICE ROUTINE” original STATUS WORD of processor is restored.

## Slide 70: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
Use of Exception in MULTITASKING
SEVERAL user programs are run at a time.
TIME SLICING is used for this : Each program is run for a small amount of time (Say ) one by one.
An Interrupt will be generated every time to switch from one process to another.

## Slide 71: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
Some Essential Functions in OS for Multitasking are listed here

## Slide 72: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
Some Essential Functions in OS for Multitasking are listed here

## Slide 73: INTERRUPTS-INTERRUPT HARDWARE
USE OF INTERRUPTS IN OPERATING SYSTEM
Some Essential Functions in OS for Multitasking are listed here

## Slide 74
DIRECT MEMORY ACCESS

## Slide 75: DIRECT MEMORY ACCESS
move DATAIN, R0
Either Processor will check STATUS flag of every device.
Or, Processor will wait for INTERRUPT from Kay board
In Both the Cases Overhead is More
What if Instead of 1 word, we need to transfer large number of data?

## Slide 76: DIRECT MEMORY ACCESS
A separate control unit to transfer without Processor Intervening for every word.
This approach is called “Direct Memory Access” (DMA).

## Slide 77: DIRECT MEMORY ACCESS
A separate control unit to transfer without Processor Intervening for every word.
This approach is called “Direct Memory Access” (DMA).

## Slide 78: DIRECT MEMORY ACCESS
A separate control unit to transfer without Processor Intervening for every word.
This approach is called “Direct Memory Access” (DMA).
1. Part of I/O Interface.
2. Responsible for I/O transfers.
3. For each word transfered it provides.
  Memory Address
  Bus signal that controls data transfer.
  Keep track of memory location (Incrementing the address) and count of number of words transfered.

## Slide 79: DIRECT MEMORY ACCESS
A separate control unit to transfer without Processor Intervening for every word.
This approach is called “Direct Memory Access” (DMA).
1. Its operation is under the control of PROGRAM BEING EXECUTED by the processor.
2. Processor will initiate by sending
  Starting address
  Number of words in block
  Direction of Transfer

## Slide 80: DIRECT MEMORY ACCESS
A separate control unit to transfer without Processor Intervening for every word.
This approach is called “Direct Memory Access” (DMA).
While Transfer is taking place.
1. Program requested for transfer will be suspended until transfer is completed (OS puts the program in BLOCKED STATE)
2. Processer may execute other programs.

## Slide 81: DIRECT MEMORY ACCESS
A separate control unit to transfer without Processor Intervening for every word.
This approach is called “Direct Memory Access” (DMA).

## Slide 82: DIRECT MEMORY ACCESS
BUS ARBITRATION
Bus Master : Device which initializes transfer.
Bus Arbitration: Transfering Bus Mastership from One Device to Another.
Bus Arbitration Types
  Centralized
  Distributed

## Slide 83: DIRECT MEMORY ACCESS
CENTRALIZED BUS ARBITRATION
Bus Controller will be a PROCESSOR or a SEPARATE UNIT attached to bus.
The controller will decide about the arbitration process

## Slide 84: DIRECT MEMORY ACCESS
CENTRALIZED BUS ARBITRATION
Bus Controller will be a PROCESSOR or a SEPARATE UNIT attached to bus.

## Slide 85: DIRECT MEMORY ACCESS
DISTRIBUTED BUS ARBITRATION
Every device participates in arbitration.

## Slide 86: DIRECT MEMORY ACCESS
DISTRIBUTED BUS ARBITRATION
Every device participates in arbitration.
0
1
1

## Slide 87: DIRECT MEMORY ACCESS
DISTRIBUTED BUS ARBITRATION
Every device participates in arbitration.
0
1
1
1
0
0
1 or 0 is 1
But as it is
The device which has sent ‘1’ will win

## Slide 88
BUSES

## Slide 89: BUSES
TYPES of BUSES
SYNCHRONOUS
ASYNCHRONOUS

## Slide 90: BUSES
TYPES of BUSES
SYNCHRONOUS
ASYNCHRONOUS
INPUT TRANSFER IN SYNCHRONOUS BUS

## Slide 91: BUSES
TYPES of BUSES
SYNCHRONOUS
ASYNCHRONOUS
INPUT TRANSFER IN SYNCHRONOUS BUS

## Slide 92: BUSES
TYPES of BUSES
SYNCHRONOUS
ASYNCHRONOUS
INPUT TRANSFER IN SYNCHRONOUS BUS with MULTIPLE CYCLES

## Slide 93: BUSES
TYPES of BUSES
SYNCHRONOUS
ASYNCHRONOUS
INPUT TRANSFER IN ASYNCHRONOUS BUS

## Slide 94
INTERFACE CIRCUITS

## Slide 95: INTERFACE CIRCUITS
I/O INTERFACE: Is the circuitry required to connect I/O device to Computer.
COMPUTER
I
N
T
E
R
F
A
C
E
P
O
R
T
BUS
TO CONNECT I/O DEVICE
TO READ/WRITE DATA FROM INTERFACE

## Slide 96: INTERFACE CIRCUITS
I/O INTERFACE: Is the circuitry required to connect I/O device to Computer.
COMPUTER
I
N
T
E
R
F
A
C
E
P
O
R
T
BUS
TO CONNECT I/O DEVICE
TO READ/WRITE DATA FROM INTERFACE

## Slide 97: INTERFACE CIRCUITS
Functions of I/O Interface:
STORAGE BUFFER: For at least one word of data.
STATUS FLAG : For processor to decide whether the BUFFER is FULL.
ADDRESS DECODING: To verify whether address sent by PROCESSOR is its own or not.
TIMING SIGNAL generation
FORMAT CONVERSION: From Bus to I/O device.

## Slide 98: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
KEYBOARD-to-PROCESSOR CONNECTION

## Slide 99: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
KEYBOARD-to-PROCESSOR CONNECTION
Generates ASCII CODE for the Key Pressed

## Slide 100: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
KEYBOARD-to-PROCESSOR CONNECTION
Key Pressed should be considered only once.

## Slide 101: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
KEYBOARD-to-PROCESSOR CONNECTION
1 when key is pressed and data is ready.

## Slide 102: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
KEYBOARD-to-PROCESSOR CONNECTION
DATAIN: ASCII value stored.
SIN: 1 when data is stored in DATAIN.

## Slide 103: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
KEYBOARD-to-PROCESSOR CONNECTION
Master Ready and Slave Ready for Asynchrous Communication

## Slide 104: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
KEYBOARD-to-PROCESSOR CONNECTION
1: Read operation
0: Write Operation

## Slide 105: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
INPUT INTERFACE CIRCUIT
8 bit Data Line

## Slide 106: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
INPUT INTERFACE CIRCUIT
32 bit Address Line

## Slide 107: INTERFACE CIRCUITS
Parallel Port
  8 bits are sent in parallel.
INPUT INTERFACE CIRCUIT
Slave Ready
Read/Write
Master Ready
Status Flag
SIN connected to DATA LINE D0

## Slide 108: INTERFACE CIRCUITS
Parallel Port
Two Types of Operations
1. Read the Status (SIN)
2.Read the Data in DATAIN
INPUT INTERFACE CIRCUIT

## Slide 109: INTERFACE CIRCUITS
Parallel Port
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.Read the Data in DATAIN (A0=1)
INPUT INTERFACE CIRCUIT
A0=0
Processor has kept address of Keyboard on address bus.
1
1
Master Ready=1
1
1
1
0
0
1
1

## Slide 110: INTERFACE CIRCUITS
Parallel Port
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.Read the Data in DATAIN (A0=1)
INPUT INTERFACE CIRCUIT
A0=0
Processor has kept address of Keyboard on address bus.
1
1
Master Ready=1
R/=1
1
1
1
0
0
1
TRI-STATE BUFFER WILL BE ACTIVATED
Processor will read SIN from Data Line D0

## Slide 111: INTERFACE CIRCUITS
Parallel Port
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.Read the Data in DATAIN (A0=1)
INPUT INTERFACE CIRCUIT
A0=1
Processor has kept address of Keyboard on address bus.
0
1
Master Ready=1
1
1
1
0
1
1
1

## Slide 112: INTERFACE CIRCUITS
Parallel Port
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.Read the Data in DATAIN (A0=1)
INPUT INTERFACE CIRCUIT
A0=1
Processor has kept address of Keyboard on address bus.
0
1
Master Ready=1
R/=1
1
1
0
1
1
1
TRI-STATE BUFFER WILL BE ACTIVATED
Processor will read DATAIN from Data Lines D0 to D7

## Slide 113: INTERFACE CIRCUITS
Parallel Port
PRINTER TO PROCESSOR CONNECTION

## Slide 114: INTERFACE CIRCUITS
Parallel Port
OUTPUT INTERFACE CIRCUIT
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.WRITE the Data to DATAOUT (A0=1 and R/)
A0=0
Processor has kept address of Printer on address bus.
Master Ready=1
1
1
1
1
1
0
1
0
1

## Slide 115: INTERFACE CIRCUITS
Parallel Port
OUTPUT INTERFACE CIRCUIT
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.WRITE the Data to DATAOUT (A0=1 and R/)
A0=0
Processor has kept address of Printer on address bus.
Master Ready=1
R/=1
1
1
1
1
0
1
0
1
TRI-STATE BUFFER WILL BE ACTIVATED
Processor will read SOUT from Data Lines D0

## Slide 116: INTERFACE CIRCUITS
Parallel Port
OUTPUT INTERFACE CIRCUIT
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.WRITE the Data to DATAOUT (A0=1 and R/)
A0=1
Processor has kept address of Printer on address bus.
Master Ready=1
0
1
1
1
1
0
1
1
0

## Slide 117: INTERFACE CIRCUITS
Parallel Port
OUTPUT INTERFACE CIRCUIT
Two Types of Operations
1. Read the Status (SIN) (A0=0)
2.WRITE the Data to DATAOUT (A0=1 and R/)
A0=1
Processor has kept address of Printer on address bus.
Master Ready=1
R/=0
0
1
1
1
1
0
1
1
TRI-STATE BUFFER WILL BE ACTIVATED
Data in lines D0-D7 are sent to PRINTER

## Slide 118: INTERFACE CIRCUITS
General 8 bit Parallel Port

## Slide 119: INTERFACE CIRCUITS
Serial Port