## Slide 1: MODULE-V PIPELINE AND VECTOR PROCESSING
By,
Mrs. Ashwini Janagal
Department of AIML
JNN College of Engineering

## Slide 2
PARALLEL PROCESSING

## Slide 3: Parallel Processing
Parallel processing is a term used to denote a large class of techniques that are used to provide simultaneous data-processing tasks for the purpose of increasing the computational speed of a computer system
The purpose of parallel processing is to speed up the computer processing capability and increase its throughput, that i.s, the amount of processing that can be accomplished during a given interval of time.

## Slide 4: Parallel Processing
SEPARATE EACH EXECUTION UNIT SUCH THAT THEY CAN OPERATE IN PARALLEL

## Slide 5: Parallel Processing
Classification according to M. J. Flynn
Single Instruction Single Data
Single Instruction Multiple Data
Multiple Instruction Single Data
Multiple Instruction Multiple DAta

## Slide 6: Pipelining
Divide Sequential Process into Sub-process.
Each subprocess belong to a segment
And segments can be executed in parallel
But there will be dependency between segments.
Output from one segment will be the Input to other segment.

## Slide 7: Pipelining
Example

## Slide 8: Pipelining
Example

## Slide 9: Pipelining
Example

## Slide 10: Pipelining
The technique is efficient for those applications that need to repeat the same task many times with different sets of data.

## Slide 11: Pipelining
TASK: TOTAL OPERATION Performed going THROUGH ALL SEGMENTS of PIPELINE
Tasks=6
Segments=4

## Slide 12: Pipelining
TASK: TOTAL OPERATION Performed going THROUGH ALL SEGMENTS of PIPELINE
Tasks=6
Segments=4
If we have
n- Tasks
k- Segments
tp clock cyle in each segment

## Slide 13: Pipelining
TASK: TOTAL OPERATION Performed going THROUGH ALL SEGMENTS of PIPELINE
Tasks=6
Segments=4
If we have
n- Tasks
k- Segments
tp clock cyle in each segment
If we have
n- Tasks
k- Segments
tp clock cyle in each segment

## Slide 14: Arithmetic Pipelining
Pipeline concept in ALU.
Mostly used for Floating point operations.
Floating point addition/subtraction can be divided into 4 parts.
  Compare the exponents.
  Align the Mantissa.
  Add/Subtract Mantissa
  Normalize the result
Example
1) 8.70 × 10-1 + 9.95 × 101
2) 8.70 × 10-1 = 0.087 × 101
3) 0.087 × 101 + 9.95 × 101
4) 10.037 × 101
5)10.037 × 101 = 1.0037 × 102

## Slide 15: Arithmetic Pipelining

## Slide 16: Instruction Pipelining
An instruction pipeline reads consecutive instructions from memory while previous instructions are being executed in other segments.
Instruction Execution Steps
  Fetch the instruction from memory.
  Decode the instruction.
  Calculate the effective address.
  Fetch the operands from memory.
  Execute the instruction.
  Store the result in the proper place

## Slide 17: Instruction Pipelining
Example:
4 Segment Instruction Pipeline

## Slide 18: Instruction Pipelining
FI: Fetch Instruction
DA: Decode and Calculates Effective Address
FO: Fetch OPerands
EX: Execute

## Slide 19: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.

## Slide 20: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
An instruction is stuck in FO because operand is still not yet generated by previous instruction
add R1, R2.
sub R2,R3

## Slide 21: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Data Dependency?
Hardware Interlock: interlock is a circuit that detects instructions whose source operands are destinations of instructions farther up in the pipeline. Such instructions will be delayed in pipeline.

## Slide 22: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Data Dependency?
Operand Forwarding: special hardware to detect a conflict and then avoid it by routing the data through special paths between pipeline segments.
Ex: If O/P of some instruction in I/P to next then O/P from ALU is passed as I/P to ALU.

## Slide 23: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Data Dependency?
Delayed Load: The compiler is designed to detect a data conflict and reorder the instructions as necessary to delay the loading of the conflicting data by inserting
no-operation instructions

## Slide 24: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Branch Difficulties?
Prefetch Target Inst.: Prefetch both possible instructions.

## Slide 25: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Branch Difficulties?
Branch Target Buffer(BTB): It is an associative memory included in the fetch segment of pipeline. It stores the target instructions and next few instructions. When branch happens instruction is readily available in BTB.

## Slide 26: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Branch Difficulties?
Loop Buffer: This is a small very high speed register file maintained by the instruction fetch segment of the pipeline. Loops are stored here with all possible branches.

## Slide 27: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Branch Difficulties?
Branch Prediction: some additional logic to guess the outcome of a conditional branch instruction before it is executed.The pipeline then begins prefetching the instruction stream from the predicted path.

## Slide 28: Instruction Pipelining
Difficulties to Implement iNstruction Pipelining
  Resource Conflict: Access to memory by different segments at same time
  Data Dependence : Instruction depends on output of previous instruction
  Branch Difficulties: Branch Instruction that will change the value of PC.
How to Handle Branch Difficulties?
Delayed Branch: In this procedure, the compiler detects the branch instructions and rearranges the machine language code sequence by inserting useful instructions that keep the pipeline operating without interruptions.