## Slide 1: MICRO-CONTROLLER AND EMBEDDED SYSTEMS (MES)

## Slide 2
ARM INSTRUCTIONS
Different ARM revisions have various instruction sets
Express capabilities of ARM processor
PRE and POST conditions
PRE <preconditions>
INSTRUCTION(s)
POST<postconditions>
No direct memory access
In case of registers, usually destination first

## Slide 3
DATA PROCESSING INSTRUCTIONS
MOVE
Arithmetic
Logical
Comparison
MULTIPLY
Operate on Registers
If suffix S is added, flags in cpsr is updated.
MOV and Logical instructions update C, N and Z flags

## Slide 4
MOVE INSTRUCTIONS
Simplest ARM instruction
Used to set initial values and transfer data between registers
Syntax:
instruction{cond}{S} Rd, N
MOV
MVN
N-register or immediate value

## Slide 5
MOV example

## Slide 6
BARREL SHIFTER
Unique and powerful feature of ARM to shift data left or right by specified positions before used in instructions
However, instructions MUL, CLZ, and QADD does not use barrel shifter!!

## Slide 7
Barrel shifter example

## Slide 8
BARREL SHIFTER OPERATIONS

## Slide 11
IMPACT OF BARREL SHIFTER ON CONDITION FLAGS

## Slide 13
Barrel shifter with cpsr update example

## Slide 14
ARITHMETIC INSTRUCTIONS
Syntax: instruction{<cond>}{S} Rd, Rn, N
Rd=Rn+N+carry
Add with Carry
ADC
Rd=Rn+N
Add without carry
ADD
Rd=N-Rn
Reverse Subtract
RSB
Rd=N-Rn-carry
Reverse Subtract with Carry
RSC
Rd=Rn-N-carry
Subtract with Carry
SBC
Rd=Rn-N
Subtract without carry
SUB

## Slide 15
Arithmetic Instruction examples

## Slide 16
Arithmetic Instruction examples

## Slide 17
Arithmetic Instruction examples

## Slide 18
Arithmetic Instruction with Barrel Shifter

## Slide 19
LOGICAL INSTRUCTIONS
Syntax: instruction{<cond>}{S} Rd, Rn, N
Rd=Rn & N
Logical bitwise AND
AND
Rd=Rn | N
Logical bitwise OR
ORR
Rd=Rn ^ N
Exclusive OR
EOR
Rd=Rn & ~N
Logical bit clear
BIC

## Slide 20
Logical Instruction Example

## Slide 21
Logical Instruction Example

## Slide 22
COMPARISON INSTRUCTIONS
Syntax: instruction{<cond>}{S} Rn, N
Rn + N
Compare negated
CMN
Rn - N
Compare
CMP
Rn ^ N
Test for equality
TEQ
Rn & N
Test bits
TST
Affects only cpsr

## Slide 23
Comparison Instructions

## Slide 24
Multiplication INSTRUCTIONS
Syntax: MLA{<cond>}{S} Rd, Rm,Rs, Rn
MUL {<cond>}{S} Rd, Rm, Rs
Rd=(Rm*Rs)+Rn
Multiply and accumulate
MLA
Rd=Rm*Rs
Multiply
MUL

## Slide 25
SIGNED MULTIPLICATION
Syntax: instruction{<cond>}{S} RdLo, ,RdHi, Rm, Rs
[RdHi, RdLo]=
[RdHi, RdLo] +(Rm*Rs)
Signed multiply accumulate long
SMLAL
[RdHi, RdLo]=Rm*Rs
Signed multiply long
SMULL
Unsigned multiply accumulate long
UMLAL
RdHi, RdLo]=Rm*Rs
Unsigned multiply long
[RdHi, RdLo]=
[RdHi, RdLo] +(Rm*Rs)
UMULL

## Slide 26
Multiplication example

## Slide 27
Multiplication example

## Slide 28
BRANCHES OF A TREE

## Slide 29
BRANCH INSTRUCTIONS
Syntax: instruction{<cond>} label | Rm
pc=label
Branch
B
pc=label
lr-return address
Branch with link
BL
Branch exchange
BX
pc=Rm & 0xfffffffe
lr=return address
Branch exchange with link
pc=Rm & 0xfffffffe
BLX

## Slide 30
Forward and backward branches

## Slide 31
BRANCH TO SUBROUTINES

## Slide 33
LOAD AND STORE INSTRUCTIONS
SINGLE REGISTER
MULTIPLE REGISTER
SWAP

## Slide 34
Register
Memory
LOAD
Register
Memory
STORE

## Slide 35
SINGLE REGISTER TRANSFER
LDR – Load Word
LDRSB – Load signed byte
LDRH – Load Half word
LDRB – Load byte
B
A
S
E
R
E G
I
S
T
E
R

## Slide 36
STR – Store Word
STRSB – Store signed byte
STRH – Store Half word
STRB – Store byte

## Slide 37
SINGLE REGISTER LOAD STORE ADDRESSING MODES

## Slide 38
Preindex with writeback

## Slide 39
Preindex

## Slide 40
Postindex

## Slide 41
OFFSET CLASSES OF SINGLE REGISTER LOAD STORE ADDRESSING MODES
SIGNED:
+/-
Scaled: Barrel shifter use with offset
Register (Rm)
Immediate (12bit)

## Slide 42
With writeback
Examples
LDR r0, [r1,#4]!
Immediate class
r0=mem32[r1+0x4]
r1=r1+0x4
LDR r0, [r1,r2]!
Register class
r0=mem32[r1+r2]
r1=r1+r2

## Slide 43
LDR r0, [r1,r2,LSR#0x4]!
Scaled class
r0=mem32[r1+(r2<<0x4)]
r1=r1+(r2<<0x4)
LDR r0, [r1,#4]
Immediate class
r0=mem32[r1+4]
r1=not updated
With writeback
Examples
Only preindex example

## Slide 44
LDR r0, [r1,r2]
Register class
r0=mem32[r1+r2]
r1=not updated
LDR r0, [r1,-r2,LSR #0x4]
Scaled class
r0=mem32[r1+-(r2<<0x4)]
r1=not updated
Only Preindex
Examples

## Slide 45
LDR r0, [r1],#4
Immediate class
r0=mem32[r1]
r1=r1+4
LDR r0, [r1],r2
Register class
r0=mem32[r1]
r1=r1+r2
Post index
Examples

## Slide 46
LDR r0, [r1],r2 LSR #0x4
Scaled class
r0=mem32[r1]
r1=r1+(r2<<0x4)
Post index
Examples

## Slide 47
Variations of STRH
STRH r0, [r1,#0x4]!
Immediate class
mem16[r1+0x4]=r0
r1=r1+0x4
Preindex with writeback
STRH r0, [r1,r2]!
Register class
mem16[r1+r2]=r0
r1=r1+r2
Preindex with writeback

## Slide 48
STRH r0, [r1,#0x4]
Immediate class
mem16[r1+0x4]=r0
r1=not updated
Preindex
STRH r0, [r1,r2]
Register class
mem16[r1+r2]=r0
r1=r1+r2
Preindex
Variations of STRH

## Slide 49
STRH r0, [r1], #0x4
Immediate class
mem16[r1]=r0
r1=r1+0x4
Postindex
STRH r0, [r1], r2
Register class
mem16[r1]=r0
r1=r1+r2
Postindex
Variations of STRH

## Slide 50
LOAD-STORE MULTIPLE REGISTER TrANSFER

## Slide 52
BEFORE LDMIA execution

## Slide 53
AFTER LDMIA execution

## Slide 54
AFTER LDMIB execution

## Slide 55
Block memory copy -ALP
loop:
LDMIA r9!, {r0-r7}
STMIA r10, {r0-r7}
CMP r9, r11
BNE loop

## Slide 56
Block memory copy example- Memory map

## Slide 58
ARM implementation of Stack
PUSH – push data to stack – STRM instruction
POP – pop data from stack – LDRM instruction

## Slide 60
ADDRESSING METHODS FOR STACK OPERATIONS
POP-LDMFA
PUSH-STMFA
Full Ascending
FA
POP-LDMFD
PUSH - STMFD
Full descending
FD
Empty Ascending
EA
POP- LDMED
PUSH - STMED
Empty Descending
ED
POP-LDMEA
PUSH-STMEA

## Slide 61
Descending Full Stack Example

## Slide 62
Descending Empty Stack Example

## Slide 63
Stack Base – starting address of the stack
Stack pointer – points to the top of the stack
Stack limit – maximum length of the stack beyond which overflow occurs

## Slide 64
SWP instruction to swap the contents of memory and register

## Slide 66
SWP Example

## Slide 67
Software Interrupts – call to OS
Format:
SWI{<cond>} SWI number

## Slide 68
SWI Example
cpsr:nzcvqift_user
pc=0x00008000
lr=0x003fffff
r0=0x12
PRE
SWI 0x123456
POST
cpsr:nzcvqIft_svc
spsr: nzcvqift_user
pc=0x00000008
lr= 0x00008004
r0=0x12
SWI_Number= <SWI Instruction> AND NOT (0xff000000)

## Slide 69
PROGRAM STATUS REGISTER INSTRUCTIONS
Registers
CPSR
SPSR
MSR
MRS

## Slide 71
WRITING EFFICIENT C PROGRAMS

## Slide 72
OVERVIEW OF C COMPILERS AND OPTIMIZATION
Optimizing code takes time and reduces readability.
Optimize the functions that are frequently executed
Optimize the functions that are important
Document non-obivious optimizations.

## Slide 73
void memclr(char *data, int N)
{
for(;N>0;N--)
{
*data=0;
data++;
}
}
Compiler does not know:
N=0
Data array pointer is 4 byte aligned
N is a multiple of 4
C compilers need to be efficient and conservative of ARM processor architecture

## Slide 74
Optimized C compilers
ARM Developer Suite
ARM target for GNU C

## Slide 75
Byte
Half word
Word
Double Word

## Slide 76
LOAD and STORE instructions by arm architecture
Pre-ARMv4: LDRB, STRB, LDR, STR
ARMv4: LDRSB, LDRH, LDRSH, STRH, STRSH
ARMv5: LDRD, STRD

## Slide 78
int checksum_v1(int *data)
{
char i;
int sum=0;
for(i=0;i<64;i++)
{
sum+=data[i];
}
return sum;
}
Check sum computation – version1

## Slide 79
checksum_v1
  MOV r2,r0; r2->data
  MOV r0,#0; r0->sum
  MOV r1, #0; r1->i
checksum_v1_loop
;r3=data[i]
LDR r3,[r2, r1, LSL #2]
ADD r1,r1,#1 ; i++
AND r1, r1,#0xff
; i=(char) casting
CMP r1, #0x40; i<64
ADD r0,r3,r0; sum+=data[i]
BCC checksum_v1_loop
MOV pc, r14 ;return sum

## Slide 80
int checksum_v2(int *data)
{
unsigned int i;
int sum=0;
for(i=0;i<64;i++)
{
sum+=data[i];
}
return sum;
}
Check sum computation – version2

## Slide 81
checksum_v2
  MOV r2,r0; r2->data
  MOV r0,#0; r0->sum
  MOV r1, #0; r1->i
checksum_v2_loop
;r3=data[i]
LDR r3,[r2, r1, LSL #2]
ADD r1,r1,#1 ; i++
CMP r1, #0x40; i<64
ADD r0,r3,r0; sum+=data[i]
BCC checksum_v1_loop
MOV pc, r14 ;return sum

## Slide 82
short checksum_v3(short *data)
{
unsigned int i;
short sum=0;
for(i=0;i<64;i++)
{
sum=(short)(sum+data[i]);
}
return sum;
}
Short Check sum computation – version3

## Slide 83
checksum_v3
  MOV r2,r0; r2->data
  MOV r0,#0; r0->sum
  MOV r1, #0; r1->i
checksum_v3_loop
ADD r3,r2, r1, LSL #1;r3=&data[i]
LDRH r3, [r3,#0];r3=data[i]
ADD r1,r1,#1 ; i++
CMP r1, #0x40; i<64
ADD r0,r3,r0; sum+=data[i]
MOV r0,r0, LSL #16
MOV r0, r0, ASR #16
BCC checksum_v1_loop
MOV pc, r14 ;return sum

## Slide 84
short checksum_v4(short *data)
{
unsigned int i;
int sum=0;
for(i=0;i<64;i++)
{
sum+=*(data++);
}
return (short)sum;
}
Check sum computation – version4

## Slide 85
checksum_v4
  MOV r2,#0; r2->sum
  MOV r1, #0; r1->i
checksum_v4_loop
LDRSH r3, [r0],#2;r3=*(data++)
ADD r1,r1,#1 ; i++
CMP r1, #0x40; i<64
ADD r2,r3,r2; sum+=r3
BCC checksum_v4_loop
MOV r0,r2, LSL #16
MOV r0, r0, ASR #16
MOV pc, r14 ;return sum

## Slide 86
Functions
short add_v1(short a, short b)
{
return a+(b>>1);
}
ans=add_v1(5,9)
Callee
Caller
Function arguments

## Slide 87
LOOPS
Efficient way of coding loops in C such that it is suitable for ARM architecture

## Slide 88
LOOPS WITH FIXED NUMBER OF ITERATIONS
int checksum_v5(int *data)
{
unsigned int i;
int sum=0;
for(i=0;i<64;i++)
{
sum+=*(data++);
}
return sum;
}

## Slide 89
checksum_v5
  MOV r2,r0; r2->data
  MOV r0,#0; r0->sum
  MOV r1, #0; r1->i
checksum_v5_loop
LDR r3,[r2],#4
ADD r1,r1,#1 ; i++
CMP r1, #0x40; i<64
ADD r0,r3,r0; sum+=data[i]
BCC checksum_v5_loop
MOV pc, r14 ;return sum
3 instructions for loop – ADD, CMP, BCC

## Slide 90
int checksum_v6(int *data)
{
unsigned int i;
int sum=0;
for(i=64;i!=0;i--)
{
sum+=*(data++);
}
return sum;
}
EFFICIENT LOOPING
Down counter

## Slide 91
checksum_v6
  MOV r2,r0; r2->data
  MOV r0,#0; r0->sum
  MOV r1, #0x40;r1->i
checksum_v6_loop
LDR r3,[r2],#4
SUBS r1,r1,#1 ; i--
ADD r0,r3,r0; sum+=data[i]
BNE checksum_v6_loop
MOV pc, r14 ;return sum
2 instructions for loop – SUBS, BNE

## Slide 92
LOOPS WITH VARIABLE NUMBER OF ITERATIONS
int checksum_v7(int *data, unsigned int N)
{
int sum=0;
for(;N!=0;N--)
{
sum+=*(data++);
}
return sum;
}

## Slide 93
checksum_v7
  MOV r2,#0; r2->data
  CMP r1,#0; r0->sum
  BEQ checksum_v7_end
checksum_v7_loop
LDR r3,[r0],#4
SUBS r1,r1,#1 ; i--
ADD r2,r3,r2; sum+=data[i]
BNE checksum_v7_loop
Checksum_v7_end
MOV r0,r2
MOV pc,r14
Extra unnecessary check

## Slide 94
LOOPS WITH VARIABLE NUMBER OF ITERATIONS
int checksum_v8(int *data, unsigned int N)
{
int sum=0;
do
{
sum+=*(data++);
}while(--N!=0);
return sum;
}

## Slide 95
checksum_v8
  MOV r2,#0; r2->data
checksum_v8_loop
LDR r3,[r0],#4
SUBS r1,r1,#1 ; i--
ADD r2,r3,r2; sum+=data[i]
BNE checksum_v8_loop
MOV r0,r2
MOV pc,r14

## Slide 96
LOOP UNROLLING

## Slide 97
Loop Overhead:
Each iteration costs: SUBS and BNE
Overhead of SUBS – 1 cycle
Overhead of BNE – 3 cycles
Total overhead – 4cycles
Hence for N iterations -> 4N cycles
Reduce the overhead by repeating loop body several times=> Loop unrolling

## Slide 98
LOOP UNROLLING
int checksum_v9(int *data, unsigned int N)
{
int sum=0;
do
{
sum+=*(data++);
  sum+=*(data++);
  sum+=*(data++);
  sum+=*(data++);
        N-=4;
}while(N!=0);
return sum;
}
Loop Overhead:
Each iteration costs 4cycles
Hence for N/4 iterations -> N cycles

## Slide 99
Road widening
Function arguments are said to be passed wide if they are not reduced to range of type.
Else they are narrow

## Slide 100
Compiler
Callee
Caller
If compiler passes wide, callee should reduce
If compiler passes narrow, caller should reduce

## Slide 101
Compiler
Caller
Callee
If compiler returns wide, caller should reduce
If compiler returns narrow, callee should reduce

## Slide 102
add_v1
  ADD r0,r0,r1,ASR #1
  MOV r0,r0, LSL #16
MOV r0, r0, ASR #16
MOV pc, r14 ;return sum
short add_v1(short a, short b)
{
return a+(b>>1);
}

## Slide 104
For addition, subtraction and multiplication no difference in signed or unsigned
For division unsigned is better
int average_v1(int a, int b)
{
return (a+b)/2;
}

## Slide 105
average_v1
  ADD r0,r0,r1
  ADD r0,r0,r0, LSR #31
MOV r0, r0, ASR #1
MOV pc, r14

## Slide 106
REGISTER ALLOCATION
If more variables exist than available registers, some variables are stored in process stack and are called Spilled variables

## Slide 107
For efficient implementation:
- minimize the number of spilled variables
- most important and frequently accessed variables are stored in registers
Limit loop variables to 12 (even though in theory 14 registers are possible)
Compiler decides spilling of variables on the basis of frequency of use.
C has register keyword.

## Slide 108
FUNCTION CALLS
APCS – ARM Procedure Call Standard – A standard for arguments and return values
In case of Thumb registers, APCS is redefined as ATPCS – ARM Thumb Procedure Call Standard

## Slide 109
Hence 4 arguments map to 4 registers
Hence for C functions having more than 4 arguments Stack will be accessed by caller and callee
To optimize, use structures in C

## Slide 110
char *queue_bytes_v1(char *Qstart, char *Qend, char *Qptr, char *data, unsigned int N)
{
do{
*(Qptr++)=*(data++);
if(Qptr==Qend)
Qptr=Qstart;
}while(--N);
return Qptr;
}

## Slide 111
char *queue_bytes_v2(Queue q, char *data, unsigned int N)
{
char *Qptr=q->qptr;
char *Qend=q->qend;
char *Qstart=q->qstart;
do{
*(Qptr++)=*(data++);
if(Qptr==Qend)
Qptr=Qstart;
}while(--N);
return Qptr;
}

## Slide 112
typedef struct
{
char *qptr;
char *qstart;
char *qend;
}Queue;
Write before functions before calling them. This allows compiler to make them inline
Critical functions can be coded as __inline keyword

## Slide 113
2 pointers are said to be alias, if they point to same address
Changing one affects another.

## Slide 114
void timers_v1(int *timer1, int *timer2, int *step)
{
*timer1+=*step;
*timer2+=*step;
}

## Slide 115
Compiler

## Slide 116
timer1
step
Alias??
Compiler performs 2 separate loads
void timers_v1(int *timer1, int *timer2)
{
int step=4;
*timer1+=step;
*timer2+=step;
}

## Slide 117
int checksum_next_packet()
{
int *data;
unsigned int i;
int N, sum=0;
data=get_next_packet(&N);
for(i=0;i<N;i++)
{
sum+=*(data++);
}
return sum;
}

## Slide 118
data
N
Alias??
Never send address of local variables
Instead make a copy and send